## Slide 1: Problems in the Forwarding Layer
draft-bryant-arch-fwd-layer-ps-00
Stewart Bryant, Uma Chunduri, Toerless Eckert and Alex Clemm

## Slide 2: Content
Problem statement draft overview
New Application -> New Needs, Services & Capabilities
Emerging Deployment Models
Forwarding Layer Shortcomings
Next Steps

## Slide 3: Content
Problem statement draft overview
New Application -> New Needs, Services & Capabilities
Emerging Deployment Models
Forwarding Layer Shortcomings
Next Steps

## Slide 4: What this Problem Statement does
Identifies an emerging set of new network and transport requirements that exceed beyond the ability of best effort protocols.
Makes a case for evolving the forwarding layer to address the new E2E needs to support 5G, B5G, 6G, Network 2030 etc.
Elaborates on problems/limitations in the forwarding paradigms based on IP and its related protocols.
Provides the first step in developing a common description and appreciation of the problems in the context of IP as the core of forwarding layer.

## Slide 5
6. Existing Protocol and Layering Challenges and Gaps . 17
6.1. Challenges with IPv6 . . . . . . . . . . . . . . 17
6.1.1. The End-to-End Model . . . . . . . . . . . . 17
6.1.2. Fixed Address Length . . . . . . . . . . . . 21
6.2. Better Than Best Effort E2E Network Services . . 22
6.3. Adaptive Bit-rate Video streaming . . . . . . . . 23
6.4. DetNet and Higher Precision Networking Service . 24
6.5. Forwarding Plane vs. Control Plane . . . . . . . 24
6.6. User-Network/Network-User Interface Signaling . . 26
7. Candidate Solution Directions . . . . . . . . . . . . 26
7.1. Variable Length Addresses . . . . . . . . . . . . 27
7.2. Address Semantics . . . . . . . . . . . . . . . . 27
7.3. Multiple Instructions . . . . . . . . . . . . . . 28
7.4. Node and Path Specific Processing Instructions . 28
7.5. Integrated Assurance and Verification . . . . . . 28
8. IANA Considerations . . . . . . . . . . . . . . . . . 29
9. Security Considerations . . . . . . . . . . . . . . . 29
10. Appendix 1: Expanded Summary of Sub-G1 Use Cases . . 29
[...]
11. Appendix 2: Expanded Summary of Sub-G2 New Network
Capabilities and Services . . . . . . . . . . . . . . 32
[...]
12. References . . . . . . . . . . . . . . . . . . . . . 40
[...]
Table of Contents
1. Introduction . . . . . . . . . . . . . . . . . . . 3
1.1. Forwarding Layer . . . . . . . . . . . . . . 4
2. New Use Cases for packet networks . . . . . . . . 5
2.1. Video and AR/VR . . . . . . . . . . . . . . . 5
2.2. Role of Fixed Networks in 5G and Beyond 5G . 6
2.3. ITU-T Focus Group Network-2030 . . . . . . . 6
3. New Network Capabilities and Services . . . . . . 8
3.1. New Services . . . . . . . . . . . . . . . . 8
3.2. New Capabilities . . . . . . . . . . . . . . 9
4. Underlying New Requirements . . . . . . . . . . . 10
4.1. Better than Best Effort . . . . . . . . . . . 10
4.2. Efficient Packet Design . . . . . . . . . . . 10
4.3. Forwarding Identifiers . . . . . . . . . . . 11
4.4. Operational visibility . . . . . . . . . . . 12
4.5. Holistic solution . . . . . . . . . . . . . . 12
5. Deployment Models . . . . . . . . . . . . . . . . 13
5.1. Edge-2-Edge Model . . . . . . . . . . . . . . 13
5.2. End-2-End Model Single Provider . . . . . . . 13
5.3. End-2-End Model with multiple Providers . . . 14
5.4. Embedded Service . . . . . . . . . . . . . . 15
5.5. Embedded Global Service . . . . . . . . . . . 16

## Slide 6: Content
Problem statement draft overview
New Application -> New Needs, Services & Capabilities
Emerging Deployment Models
Forwarding Layer Shortcomings
Next Steps

## Slide 7: New Applications drive new Needs
Beyond 5G will require URLLC beyond the radio edge and include backhaul and core.
Increasing number of mission-critical applications (tele-operation of equipment, tele-driving, tele-medicine, tactile) are not tolerant of loss and cannot afford retransmissions due to latency constraints
AR/VR and holographic networking applications require high traffic volumes with predictable latency guarantees, not just optimization.
Space-terrestrial networks with mega-clusters to ensure connectivity in airspace, over oceans, and beyond exceed the mobility capabilities of existing technologies
Resource-constrained IoT devices are hampered by the constraints of IPv6, such as address lengths

## Slide 8: New Needs (1)
5G/B5G Services – end-to-end support
  URLLC and mMTC are addressed in the radio, but not yet in the backhaul.
  The fixed network packet layer needs be developed to keep up with the new radios.
Latency precision category of service:
  Industrial Internet, industry automation, V2X, Tactile internet etc.
Volumetric Data transmission
  Immersive AR/VR media transmission - Predictable throughput (over bandwidth) is necessary for Motion to Photon latency requirements E2E 20 ms for realistic world visualizations.
  Media evolution from AR/VR to Holograms pushes capacity to 10s of gigabits.

## Slide 9: New Needs (2).
Evolution in Reachability Paradigms
  Integration of multiple space-broadband constellations with terrestrial networks. To access satellite-networks, geo-coordinate awareness for reachability.
  Edge compute service data and attributes are location specific. Network layer location awareness for service delivery.
  ManyNets (Network of many largescale non-transit networks: Sigfox, public clouds), require interworking of disparate network types.
IoT is stressed by the constraints of IPv6.

## Slide 10: New Services
High-Precision Communications Services
  Precise service-level objectives (SLOs) for e2e latency, loss
  In-time (not to exceed) & on-time (not to exceed and no sooner than permitted)
  Coordinated services (matching & interdependent service levels across flows)
Holographic and Tactile Services
Qualitative Communications Services
  Selective suppression of retransmission and dropping of payload portions

## Slide 11: New Capabilities
Manageability:
  High-precision service assurance
  Not best-effort service assurance as an afterthought
High Programmability and Agile Lifecycle:
  Rapid adaptation to new contexts, applications
Security and Trustworthiness:
  Authenticate and authorize traffic without impacting SLOs
Resilience:
  Robust to perturbations while avoiding loss or retransmits to meet mission-critical needs
Privacy-sensitive:
  Balance need for user privacy with legitimate operational needs.

## Slide 12: Content
Problem statement draft overview
New Application -> New Needs, Services & Capabilities
Emerging Deployment Models
Forwarding Layer Shortcomings
Next Steps

## Slide 13: Emerging Deployment Models
End to End over the Internet backbone is a minority of traffic
Commercial deployments do not operate the way they used to.
Application trajectory to sit in (protected) servers a few hops from the user.
Applications are becoming self-contained and use their own stack which is tunneled over UDP/IP to the server.

## Slide 14: Evolving Network Architecture Facilitates Change
CE
PE
Private
Peering
H
CE
PE
S
CE
PE
Internet Core
SP1
SP2
SP1
The classical E2E model with connectivity via the internet core is being replaced by a model with edge compute and private interconnections.
Transit AS
CE
PE
SP2
S
H
H
S
Host/client
Server
Host/client
Host/client
(Cloud) Server
(Cloud)Server
This significantly reduces the problem of rolling out new network services.
Classical E2E Internet
Evolving Internet

## Slide 15: Changing Fixed Access Models (1 or 2 Providers)
DC-FABRIC
S
S
Private Global
DCI
DC-FABRIC
S
S
DC-GW
DC-GW
ACCESS NW
H
H
Single Provider
(need for E2E IP
With additional
Service req.)
Access network and single global provider with local point of presence.

## Slide 16: Single “Underlay” provider E2E for 4G/5G network (Cellular/Access Networks)
DC-FABRIC
ACCESS NW
UE’s
H
Vehicular
H
Drone/UAV
H
IIoT
H
Phone/eMBB
RADIO (Tower)
CS-PE
Aggr-PE
Core-PE
Cellular Core Network
Internet
Service Termination
Need for E2E IP With stringent underlay needs
Global Private
Networks (DC)
DC-FABRIC
Compute/Storage
Compute/Storage

## Slide 17: Content
Problem statement draft overview
New Application -> New Needs, Services & Capabilities
Emerging Deployment Models
Forwarding Layer Shortcomings
Next Steps

## Slide 18: Addressing and Packet Formats Forwarding Layer Shortcomings (1)
Addresses are:
  Too long (eg.: IoT, LowPAN, ..)
  Too short (eg.: content semantics, SR network programming, etc)
  Always from the same address family
  Limited semantics
Packet format / extensibility / flexibility:
  Only IPv6 going forward(*): RFC8200 very challenging to meet new needs
  Only few additional types of extension headers can be added
  But not extensible enough for the network needs of the new application
  Modifying packet header metadata (beyond ECN, segment-id ?)
  For example multiple, lightweight per-path network guidance to a packet.
(*) https://www.iab.org/2016/11/07/iab-statement-on-ipv6/

## Slide 19: Beyond Best Effort (BBE) Forwarding Layer Shortcomings (2)
‘QoS’ services are limited
  Only in limited (“controlled”) domains.
  Not end-to-end and predictable (throughput, latency)
  Not granular (with DiffServ)
  Not accurate and guaranteed (even with low-latency-low-loss-services – L4S)
  Programmability
DetNet is limited by use of current data planes
  Scoped for limited to private networks amongst a set of coordinated endpoints.
  Missing full forwarding plane for IP (e.g. PREOF).
  Service model for ”inelastic” traffic only (CBR/TSPEC) traffic
Fairness and differentiated elastic traffic unresolved
  Internet Fairness == “Do not kill other flows” (not good enough)
  Component proposal exist: NADA weighted CC, PI2, Multi-TSPEC, ...
  But overall solution architecture missing.

## Slide 20: User-Network Interface (UNI) Forwarding Layer Shortcomings (3)
  UNI required to enable high-value applications
    Application needs to ask more from the network than it can today, and network needs to know more than it does today to help.
  Explicit User/Application <-> signaling missing
    BBE services (traffic specific Service-Level-Objectives)
    High Precision Network state feedback (beyond ECN framework)
Current UNI protocols designed for execution in control plane CPU
    Problem: Control plane not keeping up with speed of data-plane (scale, latency)
    Design future UNI protocols for execution in data-plane
    In data-plane signaling, e.g.: [I-D.han-tsvwg-ip-transport-qos] [I-D.han-tsvwg-enhanced-diffserv]
  Security model missing
    No trust model: User <-> Network (E.g.: application assumed to only trust DC server app)
    No comprehensive authentication: User <-> Network
    Solvable for limited (collaborating) domains – including future (Internet) Access Networks.

## Slide 21: Content
Problem statement draft overview
New Application -> New Needs, Services & Capabilities
Emerging Deployment Models
Forwarding Layer Shortcomings
Next Steps

## Slide 22: Where To Go From Here
Need converged networks with both BE and BBE
Need an architectural level discussion
  About how to address the new requirements.
  How address (inter)network changes.
Why not make piecemeal fixes ?
  X number of services, at-least X or more protocols, that much effort in design, development and standardization
   Integration then has increased complexity
Or take a step back to assess the situation
  Holistically gather and study forwarding requirements

## Slide 23: Let’s Talk
The applications and the network deployments are changing.
The economics are changing.
This is an area where the IETF needs to lead.
Feedback and contributions to this work are welcome.
  Agreements or disagreements? What have we missed? Is there anything we have overstated?
Please join us!

## Slide 24: The End